## Slide 1: How to Spot the Right Development Site & Determine its Potential Yield
Marc Terry, Parker Scanlon Surveying & Town Planning

## Slide 2: Parker Scanlon
Founded April 2007
Now employing over 20 staff members
Consultants in Surveying, Town Planning, Bushfire Assessment & Project Management
New Office – 17 William Street, Hamilton

## Slide 3: Parker Scanlon
Utilizing the latest technologies;
  GPS
  Robotic Theodolites
  UAVs (Drones)
  LIDAR

## Slide 4: Parker Scanlon
Clients Include;
  Project Home Builders
  Residential & Commercial Developers
  Local Councils
  Conveyancers
  Shopping Centre Management
  “Mum and Dad” Developers

## Slide 5: The Top Ten

## Slide 6: 1. Site Access
Legally all properties must have a road frontage for access, waste collection and provision of services;
In some cases access from a laneway may be permissible but can present issues (is the lane Publicly or Privately owned?);
Enough land to accommodate a battle-axe handle?;

## Slide 7: 2. Zoning & Lot Size
Rules change between different Council areas, check the Local Environmental Plan (LEP);
Different rules for Torrens/Strata/Community Title Subdivision;
Enabling clauses in LEPs allow smaller lot sizes when subdivision is to occur in conjunction with new dwelling construction;
SEPP 1 Objections & Clause 4.6 Variations.

## Slide 8: 3. Site Slope
Driveway Access;
Maximum slope across building envelopes;
Retaining walls – expensive and setbacks required may reduce development yield;
Requirement for a Geotechnical Report.

## Slide 9: 4. Flooding
Many parts of the Hunter Region flood effected, confirm if the land is effected with;
  Section 149 Certificate (part of most sales contracts);
  Flood Prone Land maps available on most Council websites;
  Flooding Certificate (application can be made to Council and will nominate a minimum floor levels for new development);
  In some cases a Flood Study by an independent consultant may be required (adding costs and delays).

## Slide 10: 5. Bushfire Prone Land
Majority of Lake Macquarie Council is mapped as being bushfire prone land along with many outer suburbs of Newcastle City Council;
Rural Fire Service sets guidelines for minimum setback of houses from bushland and the use of different building materials to mitigate risks;
Cannot create a subdivision lot that is in a flame zone.

## Slide 11: 6. Drainage
How will stormwater leave the site?;
A lot that slopes to the road is preferable;
A lot that slopes to the rear may require an easement/easements through neighbouring land to access Council’s trunk drainage network or a natural watercourse;
Negotiations with neighbours can add time and cost to the planning process;
Easements imposed by Court order (Section 88K).

## Slide 12: 7. Services
Dial Before You Dig (DBYD) searches are free and provide an indication of the approximate location of all known underground services;
Location of sewer most important to consider, only service that requires gravity to work;
Sewer is the service most likely to run through a lot rather than in the road reserve.

## Slide 13: 8. Easements
A site with existing Easements, Restrictions or Covenants typically have a lower yield than an unencumbered site;
Restrictions on the Use of Land may even attempt to prevent subdivision or development;
Certificate of Title lists all encumbrances but a thorough inspection of the terms of each by a suitably experienced professional may be required.

## Slide 14: 9. Mine Subsidence
Old underground mine workings under much of the land in Newcastle and surrounding Councils and are the hidden killer of many developments;
All new buildings and subdivisions within nominated Mine Subsidence Districts must be approved by the Board;
The Board provides maps of approximate district boundaries on their website and can provide some initial feedback during due diligence stage through a quick phone call.

## Slide 15: 10. Riparian Boundaries
Riparian – “related to or situated on the banks of a river”;
May assist with stormwater disposal and may improve the visual amenity of the site;
Beware, in some areas a buffer of up to 40m on either side of the watercourse may be imposed for any building work;
If a Topographic map shows a “blue line” through or adjacent to your property further investigation is required.

## Slide 16: Useful Links
SIX Maps (https://maps.six.nsw.gov.au)
Planning Portal (www.planningportal.nsw.gov.au)
Dial Before You Dig (http://www.1100.com.au)
Mine Subsidence Board (www.minesub.nsw.gov.au)

## Slide 17: Parker Scanlon – Here to Help
Mark Scanlon – Managing Director & Surveyor
Ed Munday – Surveyor & Planner
John Sorby – Surveyor
Brad Draper – Planner & Bushfire Consultant
Madeline Thomas – Planner
Marc Terry – Surveyor
www.parkerscanlon.com.au
surveys@parkerscanlon.com.au